  SOCGEN Project
Open Sourced Design for Reuse Toolset
John Eaton
Ouabache Designworks

---
Socgen
- Creates a development environment for developing component IP modules and running tool flows.
- Provides a structure for delivering it to the end user and retargeting to another technology.
- Ip-xact enabled.
- Open sourced scripts and example rtl

---
Installation and usage
- svn co -user <> -passwd <> opencores.org /ocsvn/socgen/socgen/trunk socgen
- ./tools/install/os + local tools + xilinx webpack
- make workspace
- make build_hw
- make build_sw
- make run_sims
- make build_fpgas

---
Component_name
ip-xact
designConfig , toolConfig and yellow pages
rtl
xml
component_version.xml
component_version.design.xml
component_version_config.xml
verilog
verilogSource
verilogInclude
verilogFragment
fsm
fsm tool files
views
sim
verilogLibraryFile(s)
syn
verilogLibraryFile(s)

---
Simulation
Component_name
sim
xml
component_version_tb.xml
lint
component_version_tb ( lint logs)
coverage
component_version_tb (files, reports)
icarus
version_config_test(s)
test_define
vcd_dump
wave.sav

---
Synthesys
Component_name
syn
ise
target_version_config(s)
target
lib
constraints
config
bsdl
bsdl file
debug
bit files

---
Development Environment
Socgen
Makefile
tools
install
sys
bin
projects
vendor(s)
library(s)
bin
doc
ip
component(s)
sw
program(s)
work

---
Tools and Scripts
- soc_generate
- build_veriloglib
- build_verilog
- build_fizzim
- build_register
- setup_coverage
- setup_sim_fileset
- setup_syn_fileset

---
Common Design Environment
- RTL Modules
  non synthesizable ( pads, srams, plls etc)
  clock and DFT ( metastable filter, async fixes,distribution )
  useful logic ( counters, shift registers etc)
- Bus Definitions
  system infrastructure ( clocks, resets dft)
  I/O ( pads, pad muxing)
  Everything but adhoc signals
- Simulation Functional Models
  clock,reset and interrupts
  micro and dma buses ( protocol checkers)
  external components ( UART, PS2, Memory...)